## Slide 1: UAV/S in GIS
Brookhaven College
Our 1st Flight Operation
July 2016

## Slide 2: Can we fly the campus?
July 2016 Used COTS $2000 UAS
  DJI Phantom 3 Pro
  12 mp camera
This is turn-key; everything is integrated
  Sensor and lens
  Gimbal and mount
  Flight control and positioning
  Remote Control

## Slide 3: Resources Needed
To Fly
  Aviation Consultant (licensed pilot, liaison to local controllers/airports)
  UAS
  Mission Planning app
  Viewing device (tablet)
To have accuracy
  AOI with group control points
To result in useful data
  Solid computing capability
  Image Processing capability

## Slide 4: How we spent 3 days.
Day 1 – Ground Control Points (GCPs)
  Create the targets
  Place the targets
  Capture location coordinates for targets
Day 2 – Flying and Photography
  Visually plan the missions
  Flight operations and team
Day 3 – Processing imagery
  Create data products

## Slide 5: Targets are fast, easy and cheap
Sq. Meter
Reinforced Edges
Staked
Flagged
Coordinates Captured
Plotter
GPS

## Slide 6: The GCPs
4 hours to plot and prep targets
8 hours to place and capture
1 hour to pick them up later

## Slide 7: Mission Planning
$10 app on the Apple Store
Easy to use
Plan Flight area relative to telemetry
  Battery life,
  Elevation,
  Wind and weather

## Slide 8: How did we cover the campus?
7 missions
400 feet elevation
Yielded 650 photos
5 member team
  PIC – pilot in command
  PAC – pilot at controls
  VO – visual observer (3)

## Slide 9: Image processing
Esri’s Drone2Map
3-hour process to stitch together 650 photos
Result is a 192 acre orthomosaic
2.25” pixel resolution
Search ‘BHC UAV’ in ArcGIS Online

## Slide 11: Next Steps RE: UAS and GIS @ BHC
DIY / BYO
  Hexacopter
  Marine vessel
Active courses with UAS technology
Small robotics (air, land and sea)
Pre-engineering skills
Spring 2017 Festival
More course content throughout

## Slide 12: UAV Workforce
Experience
Skills
Knowledge
Case Study applications

## Slide 13: Evolving Research and Guidelines
FAA small UAV rules
Drone technologies as platforms
Drone sensor technology

## Slide 16: Thank you
J. Scott Sires
  Geospatial Technology Program
  Professor & Coordinator
  Brookhaven College
  Mathematics & Sciences Division
  3939 Valley View Lane
  Bldg. H, H-115
  Farmers Branch, Texas, 75244
  972-860-4362
ssires@dcccd.edu www.brookhavencollege.edu/
www.dcccd.edu/gis